Guidance and checklists for NMD Salmonella detections

The purpose of this document is to assist operators to undertake the Salmonella Performance Standards (SPS) tasks specified in the National Microbiological Database Programme Specifications, Schedule 1 section 6.7.1

Group 1 and porcine Group 2– Salmonella performance standard

The current Notice and Schedule 1 document can be found in the following location:

http://www.foodsafety.govt.nz/elibrary/industry/animal-products-national-nmd/schedule-2011.pdf

For all positive Salmonella detections, operators should complete Table 1, sections (a) and (b) and Table 2 as relevant to either a first, second, third or subsequent Salmonella detection.

In addition, Table 2 provides some guidance for operator process reviews. Two Appendices are attached to provide specific details for porcine and bobby calf hygienic dressing investigations.

| TABLE 1(a): Actions for Salmonella detections |
| --- |
| Operator to complete Table 1 for all positive Salmonella detections. Attach recommended records. |
| Processor information | Processor name: RMP Identifier: Contact name: Telephone number: Email: |
| Sample information | Detection number (1st, 2nd or 3rd?) |
| Action | Comment/recommended records | Record date completed & Any additional notes |
| Inform the MAF VS verifier | Record NMD sampling date and species involved. Attach copy of laboratory result and notification to verifier |  |
| Traceback records | Attach copies of supplier declarations |  |
| Confirm the laboratory has submitted purified cultures to ESR | Record details of confirmation of sample submission to ESR and attach results of serotyping |  |
| Contact the animal health laboratories | Record details of consultation with animal health service and note whether any reported increase in salmonellosis cases |  |
| Review personnel health records | Record details of any reported salmonellosis symptoms in personnel |  |

| TABLE 1 (b): Escalating response actions for Salmonella detections |
| --- |
| To confirm all actions required for the Salmonella detection have been completed, the operator completes the following sections as applicable to a first, second and third detection. |
| First detection: | Attach or cross reference records |
| Review entire process |  |
| Identify contributing factors |  |
| Implement corrective and preventative actions (including any applicable market access requirements) |  |
| Second detection: | Attach or cross reference records |
| Complete review as for first detection |  |
| Review first detection corrective and preventative actions |  |
| Implement further corrective/preventative actions where required (including any applicable market access requirements) |  |
| Inform MAF primary verifier |  |
| Third detection: | Attach or cross reference records |
| Complete review as for first detection |  |
| Review first & second detection corrective and preventative actions |  |

| TABLE 1 (b): Escalating response actions for Salmonella detections continued |
| --- |
| Implement further corrective/preventative actions where required (including any applicable market access requirements) |  |
| Complete a Salmonella management plan describing process/HACCP reviews (submit to MAF verifier) |  |

| TABLE 2: Guidance material for operator Salmonella investigation |
| --- |
| This table describes the recommended investigation of pre-slaughter management, hygienic dressing and operator support programme review investigations. Note: Post slaughter management is not included in this check sheet. |
| Transporter Supplier’s own transport used? Other transport operators used? Truck/driver details? Time from farm to premises? Transporter vehicle cleaned between use? Transporter cleaning procedures? |  |
| Receiving and holding Flooring type in ramp/yards Holding time in yards Cross contamination between mobs Cleaning/hygiene of holding and unloading ramps/holding pens/races/restrainer equipment. |  |
| Ante-mortem examination Ante-mortem inspection issues? Stock health and suitability for hygienic processing (e.g. cleanliness)? Adequate feed withdrawal period to reduce the incidence of punctured/ruptured viscera? |  |

| TABLE 2: Guidance material for operator Salmonella investigation continued |
| --- |
| Washing Effective washing to reduce gross faecal/dirt contamination on the skin? Stock drying to avoid drip from pelt during dressing? |  |
| Slaughter and dressing (review slaughter floor hazard control as applicable to species from stun area to PM examination) Additional guidance provided for pigs (Appendix 1) and bobby calves (Appendix 2) |  |
| Support programme review | Comments |
| Review operator support programmes to identify changes or other factors that may have contributed to the Salmonella detection. Comment on process control by supervisory staff. |
| Design, construction and maintenance of buildings, facilities and equipment |  |
| Repairs and maintenance of equipment |  |
| Sanitation and cleaning of processing areas, facilities and equipment |  |
| Personnel hygiene, entry and exit of personnel |  |
| Training of personnel |  |
| Further comments or details: |  |

| Appendix 1 - Porcine slaughter and dressing guidance material Processing of pigs should be reviewed using the premises HACCP plan. The following provides some guidance on key steps where contamination and distribution may occur during dressing. |
| --- |
| Process Step | Comment |
| Sticking and bleeding | Hygienic sticking technique to minimise contamination? |  |
| Scalding | Adequate scald tank temperature to minimise bacterial load? Addition of pH modifiers – e.g. soda ash to minimise bacterial load? |  |
| Dehairing and scraping | Hygienic technique to minimise contamination? |  |
| Singeing | Effective flaming technique to reduce the micro load on the skin surface? |  |
| Scrubbing / polishing | Effective cleaning and maintenance of backscraping or polishing equipment to minimise contamination of carcasses? |  |
| Evisceration | Hygienic techniques during freeing and dropping of the bung (e.g. bagging), and prevention of puncturing the gut to minimise contamination? Note any incidence of punctured/ruptured viscera? Note any incidence of faecal spillage? Hygienic removal of contamination? |  |
| Post-mortem examination Retain trim / re-examination | Effective identification and removal of defects? Hygienic inspection procedures to minimise contamination? |  |

| Appendix 2 - Bobby calf slaughter and dressing guidance material |
| --- |
| Processing of calves should be reviewed using the premises HACCP plan. The document “An Evaluation of Young Calf Processing in New Zealand” contains useful guidance and can be located through the following link: http://www.foodsafety.govt.nz/password-protected/animal-products/meat-manuals/calf-processing/an-evaluation-of-young-calf-processing-in-nz.pdf Several recommendations were identified in the above report and should be reviewed. There should be clear justification by the operator where recommendations have not been implemented and how the risk is otherwise managed. These recommendations are listed below. If you can not open the document at the above link, ask your verifier for a copy of it. |
| Recommendation | Comment |
| An effective rectal bung should be used and preferably as soon as the procedure can be carried out. |  |
| The tail should be left entire until after the hide puller and then removed entirely prior to the ringing station |  |
| The weasand should be isolated and clipped prior to the Y cut. |  |
| If the forelegs are not shortened prior to the scales, contamination of the knuckles on the forelegs during the shifting from the wide to narrow spreaders should be minimized. |  |
| The pizzle should be clipped after the hide puller to avoid contamination transfer between the hide and pizzle to the carcase. |  |
| A ringing hook should be used so that any contact between the ringer’s hand, the anus and the carcass is eliminated. |  |
| Trimmers should be using tweezers to grasp any contamination. |  |
| Rectal contents should be contained by bagging after careful ringing and exteriorization of the anus, followed by replacement into the rectal cavity. If the bagging procedure is adopted, it must be done in an effective and hygienic manner. This procedure was viewed at one Australian premises (chain speed 8.5 per minute) and by using a plastic bag and rubber band the distal rectum was effectively sealed. |  |
| The bung set should be left attached to the colon. |  |
| Steam vacuum intervention should be used on the forequarters and areas exposed by opening cuts |  |

The table below provides further guidance material, derived from the 2011 bobby calf season review, on areas where contamination and distribution of Salmonella may occur.  It is recommended the operator completes the table as a checklist as early as practical in the bobby calf processing season.

| Process Step | Comment |
| --- | --- |
| Stockyards | Review stock washing in stockyards |  |
| Slaughter floor | Review cleaning and sanitation programme including pre-op, overheads, gut buggy etc |  |
|  | Review chain speeds and production configuration. NB: High chain speed or high utilisation of staff and equipment is a common element reported from Salmonella incidences. |  |
|  | Review hock cutter washing and sterilisation process. Eg. modify to allow greater insertion of the hock into the sterilization chamber. |  |
|  | Review techniques at Y cut ProVac and Flap Provac |  |
|  | Review carcass contact points around the hide puller sensor eg. forelegs contacting above the rail sprinkling contamination downward over the carcass. |  |
|  | Review personnel hygiene eg. protective clothing shall be kept in a clean condition or otherwise change on a regular basis. Damaged clothing shall be replaced. |  |
| Boning room | Review cleaning and sanitation programme including pre-op, overheads, bandsaws, conveyance belts. |  |
|  | Review Pre-trim results regularly. NB: System must be in place to communicate any poor results to the slaughter floor immediately. Action must be taken to identify and correct the cause(s) that could be contributing to the pre-trim results |  |
|  | Review processing environment eg. room temperatures, ventilation, water, drains, vents, personnel entry and egress |  |
| General | Review staff training programme esp. hygienic standards (hand washing, apron washing, knife washing/sterilization etc). |  |
|  | Ensure weekly meetings are conducted (as per NMD Notice 2011) with slaughter floor and boning room management and the verifier to discuss results/findings, instigate preventative measure, and ensure production schedules are tailored to minimise contamination. |  |